## Slide 1
QDM Image Super Resolution BTP
1
Biweekly Meeting
Friday, 23 October 2026
Combined-data ConvLISTA experiment
HPC setup and pilot results
By Abhay Chandra
Notes: Biweekly meeting, Friday 23 October 2026. Abhay Chandra. This update covers the expanded ConvLISTA dataset, remote GPU execution and completed two-epoch pilot. The full-training results are pending in the supplied logs.

## Slide 2
Work completed so far
2
Learned one blur operator jointly from Bx, By and Bz.
Compared ISTA, FISTA and ConvLISTA on the original coil fields.
Checked stopping criteria and the limits of direct crop pairing.
Implemented ALISTA for a separate synthetic sparse-recovery test.
Next step: expand the dataset and train one shared ConvLISTA model.
Notes: Recap of work preceding the combined-data experiment, based on the supplied biweekly and LISTA/ALISTA thesis decks and ALISTA.md. The magnetic work fitted a joint Bx/By/Bz Fourier blur operator, compared ISTA/FISTA and ConvLISTA for the original single geometry and height pair, investigated solver stopping and crop-boundary effects, and implemented a separate synthetic sparse-recovery ALISTA benchmark. Synthetic ALISTA results do not establish magnetic-field performance. This update then expands the ConvLISTA dataset and runs the comparison on remote GPU compute.
Sources
/Users/abhay/Desktop/bsp/learning_ker/presentations/LISTA_ALISTA_Thesis_Presentation.pptx; /Users/abhay/Desktop/bsp/learning_ker/presentations/biweekly_update/QDM_BTP_Biweekly_07_Oct_2026_Crop_Hypothesis_Final.pptx
/Users/abhay/Desktop/bsp/learning_ker/ALISTA.md

## Slide 3
HPC transfer and GPU setup
3
Transferred the code and both datasets to remote compute.
Moved execution from the Prajna queue to the professor’s server.
RTX A6000, 48 GB GPU memory. CUDA checks passed.
Two-epoch pilot complete. The 200-epoch experiment has started.
Notes: The project and both datasets first moved to Prajna, where queue and submission limits delayed GPU access. The actual combined experiment ran on the professor’s GPU server. One RTX A6000 has about 48 GB VRAM. The Python 3.11 / PyTorch 2.6 CUDA 12.4 environment passed FFT and gradient checks. The latest supplied log shows the 200-epoch run started, but no completed full-run results were supplied. Snapshot: 23 October 2026.
Sources
User-supplied Prajna squeue and submission errors, transfer logs, professor-server nvidia-smi, package installation and CUDA FFT/autograd check outputs in this conversation.
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.

## Slide 4
Combined data: 17 height pairs, 51 component pairs
4
Geometry | CSV planes | Reference | Height pairs | Component pairs
L1_C1 | 11 | 0.5 µm | 10 | 30
IC_4um | 7 | 0.5 µm | 6 | 18
IC_2um | 2 | 1.0 µm | 1 | 3
Total | 20 | Within geometry | 17 | 51
Pair each higher plane with its geometry’s lowest plane.
17 pairs × (Bx, By, Bz). Full 1400 × 1400 fields, with no crops.
Notes: The raw inventory contains 20 CSV planes: 11 L1_C1, 7 IC_4um and 2 IC_2um. Anchor pairing uses each geometry’s lowest available plane as reference. L1_C1 inputs z=1 through 10 µm use reference 0.5 µm. IC_4um inputs z=3,4,5,6,7,10 µm use reference 0.5 µm. IC_2um input 2 µm uses reference 1 µm. Every pair provides matched Bx, By and Bz examples. The loader validates units, finite values, complete grids and coordinate alignment, then caches float32 µT fields with checksums. These are full 1400x1400 maps, not crops. Examples share references and are correlated.
Sources
/Users/abhay/Desktop/bsp/learning_ker/hpc/combined_dataset_inventory.json
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_data.py
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 5
One shared ConvLISTA across the combined data
5
16 layers, two shared 9 × 9 filters and one scalar: 163 parameters.
Fit and freeze one Fourier operator for each of the 17 height pairs.
Normalize every input and reference by one global training scale q.
Process one full component at a time, with gradient weight 1/51.
After all 51 examples, take one Adam update and save a checkpoint.
Notes: The method extends the previous single-pair ConvLISTA without changing its 163-parameter count. Pair-specific Fourier kernels H are jointly fitted to Bx/By/Bz and then frozen. A=Crop(real(IFFT(H*FFT(Pad(x))))) with 32-pixel padding; its adjoint uses conjugate H. In normalized coordinates the update is soft at threshold s_p theta of x-s_p A_p*(A_p x-b)+C_b b+C_x x. The pair step is 0.99/max|H_p|². There are two tied bias-free 9x9 convolutional filters and one nonnegative shared scalar. Zero filters and theta=lambda/q initialize the model at ISTA for every pair. q is the maximum absolute value across all training inputs and references, preserving relative amplitudes. Predictions return to µT by multiplication by q. One full component per batch contributes normalized MSE weight 1/51. Gradients accumulate across all components before one Adam update. The model uses activation checkpointing and a blurred-field warm start.
Sources
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_lista.py
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
/Users/abhay/Desktop/bsp/learning_ker/scripts/torch_inverse.py and scripts/deblur.py
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 6
Training and comparison protocol
6
Setting | Protocol
Training budget | 2-epoch pilot, then 200 epochs
Adam / regularization | Learning rate 10⁻⁴, λ = 10⁻⁴ µT
Checkpoint selection | Minimum training MSE, including epoch 0
Classical comparisons | ISTA / FISTA at 16 updates and to tolerance
Stopping rule | Relative PG ≤ 0.001, cap 100,000 updates
Inference timing | Warm-up, then median of 3 synchronized repeats
Same training fields for evaluation. No independent validation or test split.
Notes: Defaults match the actual pilot and full-run launch: 16 layers, Adam learning rate 1e-4, gradient norm clip 1, physical lambda 1e-4 µT, 32-pixel pad, blurred initialization, batch size one and activation checkpointing. The pilot trains for 2 epochs and the new full run for 200 from the original initialization. Best post-update training MSE including epoch 0 selects the checkpoint. All pairs also enter joint reference-assisted operator fitting, so this is same-sample reconstruction, not held-out generalization. Classical methods use the same pair operator, scale, precision and GPU. Relative PG is RMS proximal-gradient mapping divided by its initial value. Stop at <=0.001 or the 100000-update cap. Timing uses one warm-up and three synchronized repeats, and the summary sums per-batch medians. Learned model loss is sharp-field MSE; ISTA/FISTA minimize the L1 reconstruction objective.
Sources
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 7
Pilot training loss
7
Chart: Normalized training MSE
| Epoch 0 | Epoch 1 | Epoch 2
Normalized training MSE | 0.0057569 | 0.0053842 | 0.0051313
10.9% lower training MSE after two epochs. Best checkpoint: epoch 2.
Notes: Exact user-reported normalized training MSE: epoch 0, 0.005756863; epoch 1, 0.0053842191; epoch 2, 0.0051312871. The reduction is approximately 10.87%. Best epoch is 2. These are only three observed points, with no independent validation curve. The vertical axis is cropped to show the small training change and is clearly labelled.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 8
Pilot reconstruction error
8
Mean range NRMSE (%) across 51 component pairs. Lower is better.
Chart: 
| ISTA 16 | FISTA 16 | ConvLISTA 16 | ISTA adaptive* | FISTA adaptive
Mean range NRMSE (%) | 4.1917 | 3.8443 | 3.9175 | 2.7368 | 2.9599
ConvLISTA: 2 training epochs. * ISTA adaptive includes 2 capped runs.
Notes: User-reported mean range NRMSE percentages across 51 component pairs: ISTA16 4.191692027391172, FISTA16 3.8442948979197764, LISTA 3.9175267933922653, adaptive ISTA 2.736754540134879, adaptive FISTA 2.9598749845343475. The chart starts at zero. Adaptive ISTA includes two unconverged capped rows, explicitly marked. All adaptive FISTA component solves converged. ConvLISTA has only two training epochs. Range NRMSE is 100*RMSE/(max reference-min reference); it is not an accuracy percentage. These are same-sample reconstruction errors.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 9
Pilot results: error and inference time
9
Method | NRMSE (%) | RMSE (µT) | Time sum (s)
ConvLISTA 16, 2 epochs | 3.918 | 14.307 | 2.264
ISTA 16 | 4.192 | 15.284 | 2.052
FISTA 16 | 3.844 | 14.006 | 2.133
ISTA adaptive* | 2.737 | 9.877 | 5,384.015
FISTA adaptive | 2.960 | 10.644 | 124.458
* Two ISTA runs reached the cap. All adaptive FISTA runs converged.
Time sum = sum of batch medians, excluding setup and file I/O.
Notes: Source: user-pasted summary.csv. Times sum medians for the 51 one-component batches, not total job walltime. Metrics exclude kernel fitting and file I/O; adaptive times include convergence checks. Each adaptive solver ran once for results, once for warm-up and three times for timing, explaining the long pilot walltime. ConvLISTA after two epochs improves on ISTA16 error, but FISTA16 retains lower error and lower measured time. The adaptive ISTA mean includes two unconverged runs. This table uses range NRMSE percent, not relative L2 or the synthetic ALISTA NMSE dB.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 10
ISTA stopping results for IC_2um
10
Input 2 µm, reference 1 µm. Convergence requires relative PG ≤ 0.001.
Component | Updates | Final relative PG | Outcome
Bx | 100,000 | 0.001398277 | Iteration cap
By | 100,000 | 0.001183943 | Iteration cap
Bz | 79,425 | 0.000999994 | Converged
Relative PG compares the remaining solver correction with its initial value.
Notes: These are the IC_2um 2-to-1 µm adaptive ISTA entries from comparison.csv. Bx:100000 updates, relative_pg 0.0013982770892834446, safety_limit. By:100000,0.0011839429761937702,safety_limit. Bz:79425,0.0009999942913851581,converged. Relative PG is the proximal-gradient RMS residual normalized to its initial value; it measures stationarity, not sharp-field reconstruction error. Bx and By are about 39.8% and 18.4% above the threshold, but this cannot be converted to a required extra iteration count. Keep the two nonconverged flags when reusing these baselines.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.
/Users/abhay/Desktop/bsp/learning_ker/scripts/torch_inverse.py and scripts/deblur.py

## Slide 11
The 200-epoch run and the next update
11
Fresh 200-epoch training has started on the same combined dataset.
Verified pilot baselines are reused, including both capped ISTA flags.
Final ConvLISTA scores and reconstruction figures are pending.
Next update: best epoch, final errors, inference time and full-field figures.
Current evaluation remains on the training fields.
Notes: The latest supplied server log confirms all 8 tests passed, baseline compatibility validation passed, epoch 0 loss was 0.005756863, epoch 1 loss 0.0053842191, and epoch 2 training started. No final full-run metrics were supplied. The full run starts from the original seed and initialization in runs/combined_full_200, leaving runs/combined_pilot intact. It reuses verified frozen physics and classical scores, times, histories, reconstructions and stopping flags. Data/source/settings/environment compatibility checks guard reuse. Future results should be read from status.json, training.json, summary.csv and metrics.json. Add per-geometry errors and field reconstruction images once available. Do not claim held-out performance: all geometry groups enter training and operator fitting. ALISTA is a separate benchmark. This slide deliberately leaves numerical results pending.
Sources
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py