## Slide 1
Transfer to HPC and GPU execution
1
Prajna: configured the environment, but GPU queue limits delayed access.
Professor’s server: transferred the code and both COMSOL datasets.
GPU: NVIDIA RTX A6000 with 48 GB memory.
Python 3.11 and PyTorch 2.6 with CUDA 12.4 passed the GPU check.
Abhay Chandra
Combined-data experiment update, 23 October 2026
Notes: This update starts with moving the existing code and both COMSOL datasets to remote compute. Prajna setup succeeded but the GPU check job remained queued, and an additional submission encountered an association submit-job limit. The professor’s server became the execution platform for the combined experiment. Do not claim the experiment ran on Prajna. The server has one RTX A6000 with about 48 GB VRAM. The successful transfer reported about 4.698 GB of raw data. Use the runtime CUDA version 12.4, not the driver’s displayed maximum CUDA capability 13.1. This is the experiment snapshot supplied on 23 October 2026.
Sources
User-supplied Prajna squeue and submission errors, transfer logs, professor-server nvidia-smi, package installation and CUDA FFT/autograd check outputs in this conversation.
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 2
Work completed before this experiment
2
Fitted one blur operator jointly from Bx, By and Bz.
Compared ISTA, FISTA and ConvLISTA on the original coil fields.
Examined stopping criteria and the limits of direct crop pairing.
Implemented ALISTA separately for synthetic sparse recovery.
This update expands the full-field ConvLISTA comparison.
Notes: The prior work established a fitted padded Fourier operator, ISTA/FISTA baselines and a 163-parameter convolutional LISTA block on the original geometry and selected height pair. The earlier crop experiments did not create independent magnetic measurements and exposed boundary artifacts. The ALISTA guide describes a separate dense synthetic sparse-recovery benchmark, not a magnetic-field result. This talk extends the ConvLISTA magnetic-field experiment only.
Sources
/Users/abhay/Desktop/bsp/learning_ker/presentations/LISTA_ALISTA_Thesis_Presentation.pptx; /Users/abhay/Desktop/bsp/learning_ker/presentations/biweekly_update/QDM_BTP_Biweekly_07_Oct_2026_Crop_Hypothesis_Final.pptx
/Users/abhay/Desktop/bsp/learning_ker/ALISTA.md

## Slide 3
What changes in the combined experiment
3
Setting | Previous experiment | Combined experiment
Supervised component pairs | 3 | 51
Geometry and height coverage | One selected height pair | 17 pairs, 3 geometries
Learned parameters | 163 | 163
Frozen Fourier operator | One per selected pair | One per pair, 17 total
Training scale | Within one pair | One scale across all training fields
One shared model learns across all geometries, heights and components.
Notes: The old selected-height experiment typically reconstructed 0.5 µm fields from 3 µm observations. The new anchor dataset uses all available higher planes with each geometry’s lowest plane as its reference. One network serves all 17 inverse problems, using a separate frozen pair operator. The number of trainable parameters is unchanged. Global normalization and operator-dependent threshold scaling are real changes. The evaluation remains same-sample reconstruction.
Sources
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_lista.py

## Slide 4
Dataset inventory
4
Geometry | Planes | Reference height | Height pairs | Component pairs
L1_C1 | 11 | 0.5 µm | 10 | 30
IC_4um | 7 | 0.5 µm | 6 | 18
IC_2um | 2 | 1.0 µm | 1 | 3
Total | 20 | Within each geometry | 17 | 51
17 height pairs × 3 signed components = 51 supervised examples
Notes: Inventory was verified by the actual CSV conversion and user-supplied server output. L1_C1 has 11 planes, IC_4um has 7, and IC_2um has 2. Anchor pairing gives 10+6+1=17 height pairs and 30+18+3=51 signed-component pairs. The raw folders remain separate in the manifest and each plane is cached once. All geometries have 1400 by 1400 grids at approximately 0.1 µm spacing. IC_2um’s reference is 1 µm.
Sources
/Users/abhay/Desktop/bsp/learning_ker/hpc/combined_dataset_inventory.json
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_data.py
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 5
How we construct the pairs
5
Choose the lowest available plane as the reference for each geometry.
Pair every higher plane with that reference, within the same geometry.
For each height pair, match Bx with Bx, By with By and Bz with Bz.
Keep every example at the full 1400 × 1400 resolution.
Example: IC_2um uses the 2 µm input and the 1 µm reference.
Notes: For L1_C1, inputs are z=1,2,3,4,5,6,7,8,9,10 µm and every reference is z=0.5 µm. For IC_4um, inputs are z=3,4,5,6,7,10 µm and reference z=0.5 µm. For IC_2um the only pair is input z=2 µm with reference z=1 µm. Each input/reference pair yields Bx-to-Bx, By-to-By and Bz-to-Bz examples. Reference planes are reused within geometries. The examples are correlated and do not constitute 51 independent geometries. This run uses full fields, not cropped patches.
Sources
/Users/abhay/Desktop/bsp/learning_ker/hpc/combined_dataset_inventory.json
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_data.py

## Slide 6
Data preparation and validation
6
Validate units, finite values and complete uniform grids.
Check matching coordinates across heights within each geometry.
Convert signed Bx, By and Bz fields to float32 arrays in µT.
Save a geometry-aware manifest with source and cache checksums.
The magnitude field |B| does not enter the linear reconstruction.
Notes: The loader checks field units, finite values, raster completeness and coordinate consistency within each geometry. It excludes the magnitude field because the linear component operator applies to signed fields. It saves float32 component arrays in µT, distinct from the older tesla cache, and records raw and prepared hashes. Geometries remain separate in the manifest. The server inventory and tests passed before the pilot launch.
Sources
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_data.py
/Users/abhay/Desktop/bsp/learning_ker/hpc/combined_dataset_inventory.json
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 7
One normalization scale for all training fields
7
q = max |B| across the training input and reference fields
b̃ = b / q x̃ref = xref / q λ̃ = λ / q
Every geometry and component uses this same scale.
Multiply predictions by q before reporting field errors in µT.
Global scaling preserves relative field amplitudes across the dataset.
Notes: q is the maximum absolute field value across every input and reference plane in the training split. Both sides of every pair use the same q, preserving their relative amplitudes. There is no per-image min-max normalization or mean subtraction. The normalized L1 coefficient is lambda_uT/q, and the final predictions are multiplied by q for physical-unit scores. In this default experiment all pairs belong to training. An optional holdout implementation would compute q using only training geometries, but that mode was not used here.
Sources
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py

## Slide 8
A frozen forward operator for each height pair
8
Aₚ(x) = Crop[Re IFFT(Hₚ · FFT(Pad(x)))]
Fit Hₚ jointly to the three signed components of each pair.
Freeze all 17 operators before network training.
Use the matching adjoint and 32-pixel padding in every method.
ISTA and FISTA minimize ½ ‖Aₚx − b‖₂² + λ ‖x‖₁.
Notes: A_p is the fixed padded convolution operator for pair p. Each transfer H_p is fitted jointly to the pair’s Bx/By/Bz fields before training and held fixed thereafter. Padding is 32 pixels and the implementation crops after each application. The adjoint uses the complex-conjugate Fourier transfer with the corresponding pad/crop boundaries. The baseline objective is 0.5||A_p x-b||² + lambda||x||1. The safe step is 0.99/max|H_p|². Because the references enter kernel fitting, this is reference-assisted same-sample evaluation.
Sources
/Users/abhay/Desktop/bsp/learning_ker/scripts/torch_inverse.py and scripts/deblur.py
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 9
One shared ConvLISTA model
9
xₖ₊₁ = soft₍sₚθ₎[xₖ − sₚ Aₚ*(Aₚxₖ − b) + C_b b + C_x xₖ]
Two shared 9 × 9 filters and one nonnegative scalar: 163 parameters.
All pairs share C_b, C_x and θ across the 16 layers.
Each pair supplies its own operator and step size sₚ.
Zero filters and θ = λ̃ initialize every pair at 16 ISTA updates.
Notes: This is the implemented normalized-field update. There are two shared bias-free 9x9 filters and one nonnegative learned scalar, totalling 163 parameters. The correction filters and threshold coefficient are tied across layers, components and pairs. The step s_p=0.99/max|H_p|² depends on the pair operator. Unlike the previous single-operator model’s direct shrinkage threshold, the shared theta is multiplied by s_p. Zero correction filters and theta=lambda_normalized exactly reproduce ISTA for every pair. The model uses a blurred-field warm start x0=b and 16 layers. No convergence guarantee is asserted for additional learned iterations.
Sources
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_lista.py
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 10
Bounded batches and one update per epoch
10
Process one full component image at a time on the GPU.
Accumulate its normalized MSE gradient with weight 1/51.
After all 51 examples, clip the gradient and take one Adam step.
Reevaluate the model and save the latest and best checkpoints.
Activation checkpointing bounds memory without cropping the fields.
Notes: Batch size one means one whole component image, not one spatial crop. One epoch iterates over the 17 pairs and their three signed components. Each component has weight 1/51 in the normalized MSE. Gradients accumulate before one clip and Adam step. This equals the intended equal-component objective, up to floating-point summation order. The implementation clips gradient norm to one and projects theta nonnegative. Activation checkpointing recomputes intermediate layers during backward to reduce activation storage. L1_C1 contributes 30/51 examples, IC_4um 18/51 and IC_2um 3/51.
Sources
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
/Users/abhay/Desktop/bsp/learning_ker/scripts/combined_lista.py
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 11
Experiment settings
11
Setting | Value
Depth and trainable parameters | 16 layers, 163 parameters
Training budget | 2-epoch pilot, then a fresh 200-epoch run
Optimizer | Adam, learning rate 10⁻⁴, gradient norm clip 1
Physical regularization | λ = 10⁻⁴ µT
Input and GPU batch | Blurred-field initialization, 1 component image
Checkpoint selection | Lowest training MSE, including epoch 0
Classical stopping | Relative PG ≤ 10⁻³, cap of 100,000 updates
All methods use the same pair operators, normalization and GPU.
Notes: The pilot used two training epochs to verify the full pipeline. The main run uses 200 epochs with the same settings and original initialization. Model selection uses minimum post-update training MSE, including epoch zero. There is no independent validation set in this run. A single component batch keeps the classical stopping decision independent per component. Lambda is in the physical µT field-unit convention before normalization.
Sources
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.

## Slide 12
Evaluation and timing protocol
12
Range NRMSE (%) = 100 × RMSE / (max xref − min xref)
Report the mean across all 51 component pairs, plus RMSE in µT.
Compare 16-update baselines and baselines run to the stopping threshold.
Timing: warm-up, then three synchronized repeats per batch.
Reported dataset time is the sum of batch medians.
Current scores measure reconstruction on the training fields.
Notes: Range NRMSE is RMSE divided by the reference’s maximum-minus-minimum, reported as a percentage. The summary averages the 51 component/pair ratios without geometry reweighting. RMSE is also reported in µT. These are same-sample results because training and joint operator fitting use the references. They do not show unseen-geometry performance. Timing uses a warm-up then the median of three synchronized repeated inference calls for each component batch. Summary time sums batch medians and excludes kernel fitting, field I/O and plotting. Adaptive timing includes stopping checks.
Sources
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 13
Two-epoch pilot training
13
Chart: 
| Epoch 0 | Epoch 1 | Epoch 2
Normalized training MSE | 0.0057569 | 0.0053842 | 0.0051313
Training MSE fell by 10.9%. The pilot selected epoch 2.
Notes: These are the exact normalized training MSE values from the user-supplied pilot log, including epoch zero before any optimization. The fall from 0.005756863 to 0.0051312871 is approximately 10.87%. The chart connects only the three observed values and must not be read as a long-run learning curve. The same initial and first-epoch values appeared in the new 200-epoch log. Validation was None throughout. Best pilot epoch was 2.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.

## Slide 14
Pilot reconstruction results
14
Mean over 51 component pairs. Lower reconstruction error is better.
Method | NRMSE (%) | RMSE (µT) | Time sum (s)
ConvLISTA 16, 2 epochs | 3.918 | 14.307 | 2.264
ISTA 16 | 4.192 | 15.284 | 2.052
FISTA 16 | 3.844 | 14.006 | 2.133
ISTA to threshold* | 2.737 | 9.877 | 5,384.015
FISTA to threshold | 2.960 | 10.644 | 124.458
* ISTA includes two runs that reached the iteration cap.
Times are sums of batch medians, excluding setup and file I/O.
Notes: All values come from the user-pasted combined_pilot/summary.csv. Full precision: LISTA NRMSE 3.9175267933922653%, RMSE 14.306568332746917 µT, time 2.264154680771753 s. ISTA16: 4.191692027391172%, 15.28417719111723, 2.0517854802310467 s. FISTA16: 3.8442948979197764%, 14.00598508236455, 2.1327676869696006 s. Adaptive ISTA: 2.736754540134879%, 9.877381577211267, 5384.015242033638 s, with two nonconverged rows. Adaptive FISTA: 2.9598749845343475%, 10.644170686310412, 124.4583948701038 s, all converged. These are mean range-normalized RMSE percentages, not relative L2 or ALISTA NMSE dB. Times sum batch medians, not total job walltime.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.

## Slide 15
Two ISTA components reached the iteration cap
15
IC_2um: input 2 µm, reference 1 µm. Required relative PG ≤ 0.001.
Component | Updates | Final relative PG | Status
Bx | 100,000 | 0.001398277 | Iteration cap
By | 100,000 | 0.001183943 | Iteration cap
Bz | 79,425 | 0.000999994 | Converged
Retain the capped results and label them as unconverged.
Notes: Only IC_2um input z=2 µm to reference z=1 µm had nonconverged adaptive ISTA results. Bx and By hit safety_limit at 100000 iterations. Bz converged at 79425. The relative PG is the RMS proximal-gradient mapping divided by its initial value. It is a stationarity measure, not reconstruction error. Bx and By ended about 39.8% and 18.4% above the tolerance, but this does not estimate the extra iterations required. All adaptive FISTA runs converged. Keep epsilon=0.001 and the two unconverged flags in any reused baseline results.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.
/Users/abhay/Desktop/bsp/learning_ker/scripts/torch_inverse.py and scripts/deblur.py

## Slide 16
What the pilot shows
16
The shared model trains across all 17 height pairs.
After two epochs, ConvLISTA improves on ISTA-16 error.
FISTA-16 still has slightly lower error and lower measured time.
Longer classical runs achieve lower mean reference error.
The 200-epoch run will test whether further training changes this comparison.
Notes: The pilot demonstrates that the pipeline can train one model over all 51 examples and save full comparison artifacts on the professor’s GPU server. Two epochs are not a mature trained-model comparison. Mean LISTA error is below ISTA16 but slightly above FISTA16. The measured summed LISTA inference time is also slightly above both fixed-depth solvers. Longer solvers attain lower average reference error, with the two ISTA stopping caveats. Minimizing the L1 objective is distinct from minimizing sharp-field MSE. No held-out generalization or super-resolution claim follows from this run.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 17
The 200-epoch experiment is in progress
17
Start a fresh 200-epoch run with the same model and training settings.
Reuse the pilot’s verified ISTA/FISTA results and frozen operators.
The latest log confirms epoch 1 completed and epoch 2 started.
Remeasure ConvLISTA after selecting the best checkpoint.
Final 200-epoch results are pending in this update.
Notes: Status is based only on the latest supplied log, not a live query. Baseline validation completed in 2.4 seconds. Initial evaluation completed and epoch 1 training/evaluation took 13.4/3.7 seconds. Epoch 2 training had started. This is a fresh run in combined_full_200, not a continuation of the pilot optimizer. It uses the same initialization and training settings and verifies baseline compatibility before training. Classical metrics, timings, reconstructions and nonconverged flags are reused from the pilot. LISTA inference and comparisons will be measured again after selecting the best model. No final full-run scores exist in the supplied evidence.
Sources
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 18
Results to update after the full run
18
Quantity | Two-epoch pilot | 200-epoch run
Completed training epochs | 2 | Pending completion
Selected epoch | 2 | Pending
Selected training MSE | 0.0051312871 | Pending
ConvLISTA mean NRMSE | 3.918% | Pending
ConvLISTA summed inference time | 2.264 s | Pending
Classical baseline results | Measured in pilot | Reuse verified pilot results
Next evidence: per-geometry errors and reconstructed field comparisons.
Notes: This editable table deliberately distinguishes observed pilot values from missing full-run values. Pending is not zero and does not imply any expected gain. Replace the pending cells using combined_full_200/status.json, training.json, summary.csv and metrics.json after completion. Classical rows will remain inherited from the pilot unless explicitly rerun under a separate protocol. Add geometry-level errors and representative field reconstructions from the saved per-pair outputs when available. No remote reconstruction image was supplied for this deck.
Sources
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)

## Slide 19
Scope of the current results
19
All 51 examples currently contribute to training and evaluation.
Repeated references and signed components make the examples correlated.
Reference fields also enter the pair-specific operator fitting.
Unseen-geometry performance requires a separate held-out experiment.
Compare the methods within this experiment before comparing with older runs.
Notes: The expanded dataset contains three geometry groups, with repeated references and three physically related signed components. It does not provide 51 independent observations of new geometries. Current kernels are jointly fitted using target fields and all pairs train the network, so claims remain same-sample. The optional analytic-operator geometry holdout is a distinct future protocol, not evidence obtained here. Old single-pair scores use a different dataset and hardware, so directly comparing their aggregate errors or times against this dataset would be misleading. Dense ALISTA synthetic results have another metric and task and are outside this comparison.
Sources
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/ALISTA.md
/Users/abhay/Desktop/bsp/learning_ker/presentations/LISTA_ALISTA_Thesis_Presentation.pptx; /Users/abhay/Desktop/bsp/learning_ker/presentations/biweekly_update/QDM_BTP_Biweekly_07_Oct_2026_Crop_Hypothesis_Final.pptx

## Slide 20
Experiment records
20
Record | Location
Dataset inventory | hpc/combined_dataset_inventory.json
Prepared data and pair manifest | runs/combined_dataset/manifest.json
Completed pilot results | runs/combined_pilot/
Full-training results | runs/combined_full_200/
Methodology and run instructions | README_COMBINED_EXPERIMENT.md
Training and comparison driver | scripts/compare_combined.py
Pilot complete. Full-training conclusions await the final saved results.
Notes: These are repository-relative or server-project-relative records for the experiment. Pilot numbers in this deck were supplied by the user in terminal output. The saved source scripts and README document implementation details, default settings and reuse checks. When final results arrive, update the full-run slides and retain the pilot identification. The original reference decks are unchanged.
Sources
/Users/abhay/Desktop/bsp/learning_ker/README_COMBINED_EXPERIMENT.md (methodology and reported pilot results; introductory pre-run wording is stale)
/Users/abhay/Desktop/bsp/learning_ker/hpc/combined_dataset_inventory.json
/Users/abhay/Desktop/bsp/learning_ker/scripts/compare_combined.py
User-supplied server outputs in this conversation, 23 October 2026: runs/combined_pilot/status.json, summary.csv, comparison.csv and combined-pilot.log. These numerical outputs were pasted by the user; the remote artifacts were not downloaded.
User-supplied combined-full-200.log on 23 October 2026: baseline validation passed, epoch 0/200 and epoch 1/200 completed, epoch 2 training started. No final 200-epoch result was supplied.